## Slide 1
Modern cyber-physical systems are not built with cyber-security in mind.
Adding cyber-security incurs runtime overheads that results in performance degradation and safety issues.
INTRODUCTION
System-level software security techniques:
  Anti-virus and intrusion-detection systems.
    monitor the entire system for indications of compromise.
Application-level software security techniques:
  Control Flow Integrity (CFI):
    Instruments the application to enforce the intended control flow at run time.
    The overhead on an application varies depending on the inputs it processes.
  The N-variant system (Double Helix1):
    Employs the systematic application of artificial diversity to prevent large classes of attacks.
    Provides formal proofs that certain classes of attacks are not possible and system can recover from attacks and continue operation.
    The performance overheads can reach up to 400%.
CYBER-SECURITY TECHNIQUES
Using Model Predictive Control (MPC).
ONLINE CONTROLLER ADAPTATION
An autonomous vehicle (AV) is tasked to complete a mission over an obstacle populated environment
The set represents the obstacle-free region of the environment and vice versa is the region occupied by obstacles.
The discrete dynamical model of the AV:
Given the constraints, the current state of the system , the desired input with no delay, and the maximum expected delay the objective is to find a control policy such that
PROBLEM FORMULATION
SIMULATONS
(a) No Overhead Delay (b) No adaptation (c) Conservative navigation (d) Adaptive navigation
Integrating Software Level Cyber Security Techniques On A Real AV:
Double Helix is used to protect ROS nodes for mapping and navigation.
Performance overhead imposed by the protected controllers reached up to 30%.
Online Adaptation Control with Unknown Overhead:
CONCLUSION AND FUTURE WORK
Trade-off between achieving high performance and maintaining safety and security constraints.
Extension to unmanned aerial vehicles (UAVs).
Use Machine Learning techniques to estimate the delays and adapt the controller input accordingly.
Mahmoud Elnaggar1, Jason D. Hiser2, Tony X. Lin3, Anh Nguyen-Tuong2, Michele Co2, Jack W. Davidson2, and Nicola Bezzo1,3
1Department of Systems and Information Engineering, 2Department of Computer Science, 3Department of Electrical and Computer Engineering
University of Virginia
Online Control Adaptation for Safe and Secure Autonomous Vehicle Operations
The delay is time varying and not known a priori.
Estimation of the delay using exponential weighted moving average algorithm (EWMA).
Unsafe regions are inflated to construct the set that satisfies the following:
Risk-based approach:
  MPC is used to compute a controller input considering maximum delay .
  A risk factor that indicates the accuracy of the last estimated delay.
  Finally, the adapted controller input is applied to the AV.
If the state of the AV lies inside the inflated region, the algorithm generates the conservative control input
Scenario | Task Execution Time(s)
No overhead | 6.3
Overhead + conservative controller | 43.4
Overhead + online adaptation | 18.1
Type of overhead | Slam_gmapping | Move_base
CPU load | 17.8% | 12.5%
Memory consumption | 3.0% | 2.56%
AHS’17
EXPERIMENTS
Without Adaptation
With Adaptation
Imposing cyclic controller runtime overheads
1M. Co, et al., “Double helix and raven: A system for cyber fault tolerance and recovery”, CISRC ’16.
Notes: TEXT TOO SMALL, at least 24 and titles 32
Consistency with fonts: use calibri everywhere
Not a Motivation but Cyber-security techniques
Problem formulation need to be trimmed down
No need to say ”the online controlelr adaptation uses model predictive control..instead say MPC to calculate the sequence of inputs
Delay is time varying and not known a priori
Estimation of delay using EWMA
Unsafe region sentence do not make sense ???? Add figure on the side of the equation
Last column: Remove Simulations and Experiemnts and just put Simulations and then experiments
Shrink the table…too much space
Remove ”we” ..it’s a poster…go doirectly to the point
What’s ML?
Add delay patetrn near figure of delay in simulation
Add titles on each snapshot